## Slide 1
ALTAIR: High-Altitude, Low-Cost Micro-Airships for “Workhorse” Precision Rubin Observatory Calibration & Beyond
Justin Albert
University of Victoria
jalbert@uvic.ca

## Slide 2
Known
view angle
Basic Technique & Goal: A 0.1% Calibrated, Mobile Source Above the Atmosphere
Integrating
sphere
Balloon Payload
440 nm
532 nm
658 nm
830 nm
100 mW lasers
Well-characterized
Lambertian spatial profile
Telescope
NIST- & NRC-calibrated (~ 0.1% absolute)
photodiode spectral response
10/23/2024 ALTAIR J. Albert 2
NIST-calibrated
photodiodes

## Slide 3
Basic Payload Design
10/23/2024 ALTAIR J. Albert 3

## Slide 4
10/23/2024 ALTAIR J. Albert 4
Can be swapped out for 635 nm or 780 nm.
Can be swapped out for 808 nm or 850 nm.
Light Sources & Calibrated Monitoring Photodiodes on 2” ID Integrating Sphere
Can be swapped out for 405 nm.
Can be swapped out for 520 nm.
Four WorldStarTech 100 mW laser diode modules, respectively 440 nm, 532 nm, 658 nm, & 830 nm, each fiber coupled into a fused-ends, “quadfurcated” MM optical fiber (custom fab’d by Ceramoptec).
One photodiode is a Hamamatsu S12698-01 (Si) and the other is a Hamamatsu G10899-03K (InGaAs).
(Utilizing two different photosensor material technologies is a useful cross-check.)

## Slide 5
Photodiode readout and digitization
10/23/2024 ALTAIR J. Albert 5
The precison heart of the mission…

## Slide 6
Payload
10/23/2024 ALTAIR J. Albert 6

## Slide 7
Flight control – AIFCOMSS
10/23/2024 ALTAIR J. Albert 7
ALTAIR Integrated Flight Control, Operation, Monitoring, & Simulation System
Code actively maintained / updated at:
https://github.com/ProjectALTAIR/AIFCOMSSwithCUPredictorTest

## Slide 8
Onboard transponder (uAvionix ping900XR)
10/23/2024 ALTAIR J. Albert 8
For continuous real-time communication with and identification to air traffic control.
(FAA & Transport Canada certified.)
So that we don’t get shot down by NORAD!!! ;)
(Or by the Chilean air force!!!)

## Slide 9
Operations & McGill / Montreal Test Flights
10/23/2024 ALTAIR J. Albert 9
910 MHz portable directional ground antennas, range approx. 100 km.
Always ≥ 2 ground stations in contact.

## Slide 10
Conclusions
10/23/2024 ALTAIR J. Albert 10
Artificial sources can in principle provide up to two orders of magnitude better photometric calibration precision than any stellar, non-solar light sources can presently.
  1) Can study them right in the lab before and after use, unlike stars.
  2) Can monitor them in-situ, in real time.
  3) Can also be used to calibrate white dwarfs (and other stars, and the Moon) very precisely, and on a detector-based standards scale.
  4) Small balloons are inexpensive!!!
  5) Fully observer-controlled choice of spectrum & color on demand, … and brightness, …exact location in the sky as function of time of night (or day), …
Not restricted to optical/IR!: e.g. a precisely-polarized Gunn diode-based precision microwave polarimetry calibration source could also be flown. (Radio, near-UV…)
Balloons, of course, do not replace additionally having a satellite source to (at
least occasionally!) determine effects from the very top of the atmosphere!!!
But ALTAIR-style balloons can (and I posit will!) be the low-cost, ground-
based-observatory-owned, workhorses.
E.g.: Rubin could own 3 or so!!! – launching them at dusk each night, flying to different areas of the sky, and having them return home at dawn each morning!

## Slide 11
Some separate & additional conclusions (backup slide)
10/23/2024 ALTAIR J. Albert B1
A very interesting (& very useful) fact about Earth’s atmosphere is that, at mid-latitudes, winds in the upper troposphere statistically tend to be in opposite direction to winds in the lower stratosphere.
Thus, with just very small amounts of (weather-optimized) upward and downward propulsion (just above and below the tropopause), powered using very lightweight flexible solar panels on top of the balloon (+ onboard rechargeable LiPoly batteries for nighttime power), one could utilize the winds to circulate near the tropopause over a given region of Earth (e.g., over a region the size of Illinois, or of Vancouver Island, etc).
After a few weeks, a significant fraction of the helium would diffuse through the balloon latex, and the balloon would descend to base for (simple and low-cost!: latex balloons are about $150) balloon and helium replacement. Then, balloon and payload would be sent back up again.
This opens up many additional, very different usage possibilities:
  Communication: replacing the need for cell-phone towers with very wide coverage balloons in remote (or not-so-remote) areas.
  Earth observation (for, e.g., long-term studies of Arctic ice, etc.)
  …… !